## Slide 1: 1G eth UDP IP stack
Simplified implementation from the FIX.QRL stables
(contributor – Peter Fall)
V2.0

## Slide 2: Features
Implements UDP, IPv4, ARP protocols
Zero latency between UDP and MAC layer
  (combinatorial transfer during user data phase)
  See simulation diagram below
Allows full control of UDP src & dst ports on TX.
Provides access to UDP src & dst ports on RX (user filtering)
Couples directly to Xilinx Tri-Mode eth Mac via AXI interface
Separate building blocks to create custom stacks
Easy to tap into the IP layer directly
Supports TX and RX with IP layer broadcast address
Separate clock domains for tx & rx paths
Choice of smaller single slot ARP or multislot up to 255 slots
Tested for 1Gbit Ethernet, but applicable to 100M and 10M

## Slide 3: Simulation diagram showing zero latency on receive

## Slide 4: Limitations
Does not handle segmentation and reassembly
  Assumes packets offerred for transmission will fit in a single ethernet frame
  Discards packets received if they require reassembly

## Slide 5: Overall Block Diagram
UDP_Complete_nomac
UDP TX bus
UDP RX bus
IP RX bus
Clocks, controls & reset
MAC TX bus
MAC RX bus
Our IP & MAC addr
Arp & IP pkt count
Generics (see block level descriptions)
CLOCK_FREQ
ARP_TIMEOUT
ARP_MAX_PKT_TMO
MAX_ARP_ENTRIES

## Slide 6: Structural Decomposition
UDP TX bus
UDP RX bus
IP RX bus
Clocks, controls & reset
Our IP & MAC addr
Arp & IP pkt count
MAC TX bus
MAC RX bus
UDP_Complete_nomac
UDP_TX
UDP_RX
IP_Complete_nomac
Tx_arbitrator
arp
IPV4_TX
IPV4_RX
IPv4
req
rsp
rx
tx

## Slide 7: ARP block options
ARP can be instantiated in one of the following options:
  arp – simple 1-slot ARP layer with timeout
  arpv2 – multislot ARP layer with timeout
These can be selected in the IP_Complete_nomac.vhd file by commenting out the appropriate line –
-- for arp_layer : arp use entity work.arp; -- single slot arbitrator
for arp_layer : arp use entity work.arpv2; -- multislot arbitrator

## Slide 8: ARP V2 Block
REQ RSP
control
IP RX bus
Arp & IP pkt count
TX
RX
arpv2
req
sync
store
arp_TX
arp_RX
clear
lookup
write
sync
RX clock domain
TX clock domain
Legend:

## Slide 9: Interface
entity UDP_Complete_nomac is
Port (
-- UDP TX signals
udp_tx_start : in std_logic; -- indicates req to tx UDP
udp_txi : in udp_tx_type; -- UDP tx cxns
udp_tx_result : out std_logic_vector (1 downto 0); -- tx status (changes during tx)
udp_tx_data_out_ready: out std_logic; -- indicates udp_tx is ready to take data
-- UDP RX signals
udp_rx_start : out std_logic; -- indicates receipt of udp header
udp_rxo : out udp_rx_type;
-- IP RX signals
ip_rx_hdr : out ipv4_rx_header_type;
-- system signals
rx_clk : in STD_LOGIC;
tx_clk : in STD_LOGIC;
reset : in STD_LOGIC;
our_ip_address : in STD_LOGIC_VECTOR (31 downto 0);
our_mac_address : in std_logic_vector (47 downto 0);
control : in upd_control_type;
-- status signals
arp_pkt_count : out STD_LOGIC_VECTOR(7 downto 0); -- count of arp pkts received
ip_pkt_count : out STD_LOGIC_VECTOR(7 downto 0); -- number of IP pkts received for us
-- MAC Transmitter
mac_tx_tdata : out std_logic_vector(7 downto 0); -- data byte to tx
mac_tx_tvalid : out std_logic; -- tdata is valid
mac_tx_tready : in std_logic; -- mac is ready to accept data
mac_tx_tfirst : out std_logic; -- indicates firstbyte of frame
mac_tx_tlast : out std_logic; -- indicates last byte of frame
-- MAC Receiver
mac_rx_tdata : in std_logic_vector(7 downto 0); -- data byte received
mac_rx_tvalid : in std_logic; -- indicates tdata is valid
mac_rx_tready : out std_logic; -- tells mac that we are ready to take data
mac_rx_tlast : in std_logic -- indicates last byte of the trame
);
end UDP_Complete_nomac;

## Slide 10: The AXI interface
This implementation makes extensive use of the AXI interface (axi.vhd):
package axi is
type axi_in_type is record
data_in : STD_LOGIC_VECTOR (7 downto 0);
data_in_valid : STD_LOGIC; -- indicates data_in valid on clock
data_in_last : STD_LOGIC; -- indicates last data in frame
end record;
type axi_out_type is record
data_out_valid : std_logic; -- indicates data out is valid
data_out_last : std_logic; -- indicates last byte of a frame
data_out : std_logic_vector (7 downto 0);
end record;
end axi;

## Slide 11: MAC Interface
The MAC interface is fairly simple with separate clocks for receiver and transmitter. Each interface (RX and TX) is based on the AXI interface and has an 8-bit data bus, a valid signal, a last byte signal, and a backchannel signal to indicate that the other end is ready to accept data.
The Transmit interface has an additional signal (mac_tx_tfirst) which can be used by MAC blocks that need something to indicate the start of frame. This signal is asserted simulaneous with the first byte to be transmitted (providing that tready is high).
On the following diagram, tx_clk and rx_clk are shown sourced from the MAC transmit and receive blocks, but can come from an independent clock generator that feeds clocks to both the MAC blocks and the UDP_IP_stack. Data is clocked on the rising edge.
UDP_IP_Stack
Data (7..0)
valid
first
last
ready
MAC Transmit
MAC Receive
Data(7..0)
valid
last
ready
tx_clk
rx_clk

## Slide 12: Synthesis Stats
451 occupied slices on Xilinx xc6vlx240t (1%)
(687 flipflops, 1294 LUTs)
Test synthesis using
  Xilinx ISE 13.4
Architecture | Slices | FF / LUTS | Block Rams | % slices used
Arp (1 slot) | 490 | 684/ 1283 | 0 | 1%
Arpv2 (255 slot) | 674 | 1139 / 1822 | 2 | 1%

## Slide 13: Module Description: UDP_complete_nomac
Simply wires up the following blocks:
  UDP_TX
  UDP_RX
  IP_Complete_nomac
Propagates the IP RX header info to the UDP_complete_nomac module interface.

## Slide 14: Module Description: UDP_TX and UDP_RX
UDP_TX:
  Very simple FSM to capture data from the supplied UDP TX header, and send out a UDP header.
  Asserts data ready when in user data phase, and copies bytes from the user supplied data.
  Assumes user will supply the CRC (specs allow CRC to be zero).
UDP_RX
  Very simple FSM to parse the UDP header from data supplied from the IP layer, and then to send user data from the IP layer to the interface (asserts udp_rxo.data.data_in_valid).
  Discards IP pkts until it gets one with protocol=x11 (UDP pkt).

## Slide 15: Module Description: IPv4
Simply wires up the following blocks:
  IPv4
  ARP
  Tx_arbitrator
Arp reads the MAX RX data in parallel with the IPv4 RX path. ARP is looking for ARP pkts, while IPv4 is looking for IP pkts.
IPv4 interacts directly with ARP block during TX to ensure that the transmit destination MAC address is known.
TX_arbitrator, controls access to the MAC TX layer, as both ARP and IPv4 may want to transmit at the same time.

## Slide 16: Module Description: IPv4_TX
IPv4_TX comprises two simple FSMs:
  to control transmission of the header and user data
  to calculate the header checksum
To use,
  set the TX header, and assert ip_tx_start.
  The block begins to calculate the header CRC and transmit the header
  Once in the user data stage, the block asserts ip_tx_data_out_ready and copies user data over to the MAC TX output

## Slide 17: Module Description: IPv4_RX
Simple FSM to parse both the ethernet frame header and the IP v4 header.
Ignores packets that
  Are not v4 IP packets
  Require reassembly
  Are not for our ip address and are not for the broadcast address
Once all these checks are satisfied, the rx header data: ip_rx.hdr is valid and the module asserts ip_rx_start.
Received user data is available through the ip_rx.data record.

## Slide 18: Module Description: arp (single slot version)
Handles receipt of ARP packets
Handles transmission of ARP requests and timeout if no response received
Handles request resolution (check ARP cache and request resolution if not found)
Three FSMs, one for each of the above functions
ARP mapper cache is only 1 deep in this implementation
  which means that it is only really good for point-point comms.
  Use ARPv2 if you want an implementation with more slots
Input signals to module indicate our IP and MAC addresses
ARP timeout is configured by generics in the ARP, IP, and UDP modules:
CLOCK_FREQ : integer := 125000000; ARP_TIMEOUT : integer := 60
CLOCK_FREQ is used to scale the rx_clk to produce a 1Hz signal for timing.
ARP_TIMEOUT specifies the timeout in seconds.
Note: on timeout, ARP does not retransmit the ARP req, but reports a transmit error.
Send again, to send extra ARP requests.

## Slide 19: Module Description: arpv2 (multi slot version)
Handles receipt of ARP packets
Handles transmission of ARP requests and timeout if no response received
Handles request resolution (check ARP cache and request resolution if not found)
Decomposed into modules:
req - handles request response protocol and contains a single slot cache for fast lookup store - maintains a map of IP->MAC addresses, configurable size to 255 tx - encodes the «I Have» and «who has» ARP tx formats rx - decodes the ARP protocols «I have» and «who has» sync - performs clock sync between the RX and TX clock domains
ARPV2 mapper cache is configurable up to 255 slots.
Input signals to module indicate our IP and MAC addresses
ARP ARP_MAX_PKT_TMO2 is configured by generics in the ARP, IP, and UDP modules:
CLOCK_FREQ : integer := 125000000; ARP_TIMEOUT : integer := 60 ARP_MAX_PKT_TMO : integer := 5 MAX_ARP_ENTRIES : integer := 255
CLOCK_FREQ is used to scale the rx_clk to produce a 1Hz signal for timing.
ARP_TIMEOUT specifies the timeout in seconds.
ARP_MAX_PKT_TMO specifies the number of received “I Have” ARP responses which don’t satisfy our request before timeout.
Note: on timeout, ARP does not retransmit the ARP req, but reports a transmit error.
Send again, to send extra ARP requests.
MAX_ARP_ENTRIES specifies the number of slots in the ARP cache (max 255)

## Slide 20: Module Description: tx_arbitrator
FSM to arbitrate access to the MAC TX layer by
  IP TX path
  ARP TX path
One of the sources requests access and must wait until it is granted.
Priority is given to the IP path as it is expected that that path has the highest request rate.

## Slide 21: Simulation
Every vdhl module has a corresponding RTL simulation test bench.
Additionally, there are simulation test benches for various module integrations.
In this version, verification is not completely automatic. The test benches test for some things, but much is left to manual inspection via the simulator waveforms.

## Slide 22: TestBench - HW
The HW testbench is built around the Xilinx ML-605 prototyping card.
It directly uses the card’s 200MHz clocks, Eth PHY (copper) and LEDs to indicate status.
A simple VHDL driver module for the stack replies with a canned response whenever it receives a UDP pkt on a particular IP addr and port number.
The Xilinx LogiCORE IP Virtex-6 FPGA Embedded Tri-Mode Ethernet MAC v2.1 is used to couple the UDP/IP stack to the board’s Ethernet PHY. This is used with the standard FIFO user buffering (which adds a one-frame delay). It should be possible also to remove this FIFO to reduce latency.
A laptop provides stimulus by way of one of two Java programs:
  UDPTest.java – writes one UDP pkt and waits for a response then prints it
  UDPTestStream.java – writes a number of UDP pkts and prints responses
The test network is a single twisted CAT-6 cable between the laptop and the ML-605 board.
Wireshark (on the laptop) is used to capture the traffic on the wire (sample pcap files are included)

## Slide 23: Test Setup
UDP_Complete_nomac
UDP TX
UDP RX
Clocks & reset
IP & MAC set
Arp & IP pkt count: 4 leds each
Xilinx mac_block
TX response process
Xilinx ML605 board
Async TX Pushbutton
Eth PHY
Java Test Code running on Laptop
UDP_integration_example
network

## Slide 24: Testbench HW - ML605 modules
UDP_Complete – integration of UDP with a mac layer
IP Complete – integration of IP layer only with a mac layer
UDP_Integration_Example – test example with vhdl process to reply to received UDP packets

## Slide 25: Test Results
The xilinx MAC layer used contains a FIFO which therefore introduces a 1 frame delay.
  For tightly coupled low latency requirements, this can be removed.
Output from UDPTest:
  Sending packet: 1=45~34=201~18=23~ on port 2000 Got [@ABC]
Output from UDPTestStream:
  … Sending price tick 205 Sending price tick 204 Sending price tick 203 Sending price tick 202 Got [@ABC] Got [@ABC] Got [@ABC] Got [@ABC] …